Ausschreibungstext

Artikelnummer

200418

Typ

AXIS Q7414

Kurzbeschreibung

Video Netzwerk Server, 4 Kanäle, H.264, MJPEG, 720x576, Karte, 12VDC

Hauptmerkmale

4-Kanal 19" Einschub-Videoserver

High-Density Lösung

Hervorragende Videoqualität

Konfigurierbare H.264 und MJPEG-Streams

4 Audio-Kanäle mit Audio-Erkennung

Unterstützt Stereo-Mikrofone

Anpassung der Bildeinstellungen

D1-Auflösung (720x576 in PAL)

Erweiterte Video-Bewegungserkennung

Manipulations-Alarmauslösung

Zum Einbau in 19"-Gehäuse Q7900 geeignet

Weitere Merkmale (Spezifikationen)

| Serie | Axis Q74 |
| --- | --- |
| Bildauflösung max. | 720x576 |
| Bildübertragungsrate max. | 25 fps |
| Videoeingänge (Anzahl) | 4 |
| Kompressionsverfahren | H.264, M-JPEG |
| Alarmeingänge | 8 |
| Audiounterstützung | ja |
| Ethernet-Schnittstelle | 1000Base-T |
| Steuer-Schnittstellen | RS-485, RS-422 |
| Interner Speicher | nein |
| 19 Zoll einbaufähig | ja |
| Stromversorgung | 12VDC |
| Leistungsaufnahme | 13W |
| Temperaturbereich (Betrieb) | 0°C ~ +45°C |
| ONVIF | ja |
| Hersteller-Nr. | 0354-001 |

Zubehör

| AXIS T8640 POE+ OVER COAX KIT | Medienkonverter, RJ45, BNC, Ethernet über Koax, PoE+, Base-/Device Set (2 Stück) |
| --- | --- |
| AXIS T8129 POE EXTENDER | PoE Extender, PoE, PoE+ kompatibel, RJ45, 100m Reichweite |
| AXIS T8604 MEDIA CONVERTER SWI | Ethernet Medienkonverter, 2x 10/100Mbps RJ45, 2x 100/1000Mbps SFP |
| AXIS Q7920 | Video Encoder Rack, 19"/5HE, 14 Hotswap Einschübe, RS-485, 4x SFP Slot, Aluminium |
| AXIS COMPANION VMS | Video Management Software, für 16 Axis Kameras, kostenlose Freeware |
| AXIS T8646 POE+ OVER COAX KIT | PoE+ OVER COAX Set, 6-Kanal: 1x T8646 POE+ OVER COAX BLADE, 6x T8642 POE+ OVER COAX DEVICE |
| AXIS T8310 CONTROL BOARD | Kontrollcenter, modular, mit Keypad, Joystick, Jog Dial |
| ACS CORE DEVICE E-LICENSE | Axis Camera Station Software, Version 5.x Core Device, E-Lizenz, 1 Kanal |
| ACS UNIVERSAL DEVICE E-LICENSE | Axis Camera Station Software, Version 5.x Universal Device, E-Lizenz, 1 Kanal |
| ACS 1 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 1 Kanal |
| ACS 4 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 4 Kanal |
| ACS 16 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 16 Kanal |
| ACS 32 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 32 Kanal |
| ACS 1 UNIVERSAL DEVICE LICENSE | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 1 Kanal |
| ACS 4 UNIVERSAL DEVICE LICENSE | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 4 Kanal |
| ACS 10 UNIVERSAL DEVICE LIC | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 10 Kanal |
| ACS 20 UNIVERSAL DEVICE LIC | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 20 Kanal |
| AXIS 4IN1 SECURITY SCREWDRIVER | Schraubendreher Set, 4-in-1, Biteinsätze pasend für Axis Produkte, inkl. Tasche |