Ausschreibungstext

Artikelnummer

200884

Typ

AXIS M7014

Kurzbeschreibung

Video Netzwerk Server, 4 Eingänge, H.264, MJPEG, 720x576, microSD-Slot, PoE

Hauptmerkmale

4-Kanal Video Encoder

Simultane H.264 und MJPEG Streams

Hervorragende Videoqualität

Auflösung: 720x576 Pixel (D1)

Hochauflösende Quad-Darstellung

1x microSD/-SDHC/-SDXC Slot für lokale Speicherung

Intelligente Videofunktionen

Spannungsversorgung: 8-20VDC, PoE

Für Wandmontage geeignet

ONVIF konform

Weitere Merkmale (Spezifikationen)

| Serie | Axis M70 |
| --- | --- |
| Bildauflösung max. | 720x576 |
| Bildübertragungsrate max. | 15 fps |
| Videoeingänge (Anzahl) | 4 |
| Kompressionsverfahren | H.264, M-JPEG |
| Alarmeingänge | nein |
| Audiounterstützung | nein |
| Ethernet-Schnittstelle | 10Base-T, 100Base-TX |
| Steuer-Schnittstellen | RS-485, RS-422 |
| Interner Speicher | microSDHC-Karte, microSD-Karte, microSDXC-Karte |
| 19 Zoll einbaufähig | nein |
| Stromversorgung | PoE, 8-20VDC |
| Temperaturbereich (Betrieb) | 0°C ~ +50°C |
| ONVIF | ja |
| Hersteller-Nr. | 0415-002 |

Zubehör

| AXIS T91A02 DIN RAIL CLIP 86MM | DIN Rail Clip, für Axis M7014, P7214 |
| --- | --- |
| AXIS T8640 POE+ OVER COAX KIT | Medienkonverter, RJ45, BNC, Ethernet über Koax, PoE+, Base-/Device Set (2 Stück) |
| AXIS T8129 POE EXTENDER | PoE Extender, PoE, PoE+ kompatibel, RJ45, 100m Reichweite |
| AXIS T8604 MEDIA CONVERTER SWI | Ethernet Medienkonverter, 2x 10/100Mbps RJ45, 2x 100/1000Mbps SFP |
| AXIS T91A03 DIN RAIL CLIP B | Schienenklemme zur Montage auf Standard 35mm DIN-Schiene, für Axis Encoder |
| AXIS COMPANION VMS | Video Management Software, für 16 Axis Kameras, kostenlose Freeware |
| AXIS T8646 POE+ OVER COAX KIT | PoE+ OVER COAX Set, 6-Kanal: 1x T8646 POE+ OVER COAX BLADE, 6x T8642 POE+ OVER COAX DEVICE |
| AXIS MICROSDXC CARD 64GB | Speicherkarte, microSDXC, 64GB, Class 10, 20 MB/s, inkl. SD-Adapter, Axis zertifiziert |
| AXIS MICROSDXC CARD 64GB 10PCS | Speicherkarte, microSDXC, 64GB, 20 MB/s, inkl.SD-Adap., Axis zertifiziert, 10 Stück |
| AXIS T8310 CONTROL BOARD | Kontrollcenter, modular, mit Keypad, Joystick, Jog Dial |
| ACS CORE DEVICE E-LICENSE | Axis Camera Station Software, Version 5.x Core Device, E-Lizenz, 1 Kanal |
| ACS UNIVERSAL DEVICE E-LICENSE | Axis Camera Station Software, Version 5.x Universal Device, E-Lizenz, 1 Kanal |
| ACS 1 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 1 Kanal |
| ACS 4 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 4 Kanal |
| ACS 16 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 16 Kanal |
| ACS 32 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 32 Kanal |
| ACS 1 UNIVERSAL DEVICE LICENSE | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 1 Kanal |
| ACS 4 UNIVERSAL DEVICE LICENSE | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 4 Kanal |
| ACS 10 UNIVERSAL DEVICE LIC | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 10 Kanal |
| ACS 20 UNIVERSAL DEVICE LIC | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 20 Kanal |
| AXIS SURVEILLANCE CARD 64 GB | Speicherkarte, microSDXC, 64GB, Class 10, 20 MB/s, inkl. SD-Adapter, Axis zertifiziert |
| AXIS SURVEILLANCE CARD 128G | Speicherkarte, microSDXC, 128GB, Class 10, 30 MB/s, SD-Adapter, Axis zertifiziert |
| AXIS 4IN1 SECURITY SCREWDRIVER | Schraubendreher Set, 4-in-1, Biteinsätze pasend für Axis Produkte, inkl. Tasche |