Ausschreibungstext

Artikelnummer

220269

Typ

AXIS Q1659 BAREBONE

Kurzbeschreibung

Netzwerkkamera, Tag/Nacht, ohne Objektiv, 5472x3648, SFP, EF/EF-S Mount, PoE, 8-28VDC

Hauptmerkmale

Netzwerkkamera mit 22,4x15mm APS-C CMOS-Sensor

Digital Single-Lens Reflex (DSLR) Imaging Technology

Canon EF Mount für professionelle EF/EF-S Objektive

Ultra HD 2160p@25fps, 3840x2880@15fps, 5472x3648@8fps

True Day&Night mit schaltbarem IR-Sperrfilter

Empfindlichkeit: 0,04 lux F1.2 (Farbe)

H.264 mit Axis? Zipstream Technology

RS422/RS485 Schnittstelle zur SNK-Steuerung

SFP Slot für optionale Glasfaseranbindung

PoE IEEE 802.3af/802.3at Type 2 Class 4, 20?28 V DC

Für Innenanwendung, optional Außengehäuse erhältlich

Weitere Merkmale (Spezifikationen)

| Serie | Axis Q16 |
| --- | --- |
| Auflösungsstandard | 20 Megapixel, Ultra HD 2160p |
| System | True Day&Night |
| Chipgröße | 22,4 x 15,0 |
| Aufnahmesensor | CMOS |
| Videokompression | H.264 |
| Bildauflösung max. | 5472x3648 |
| Bildübertragungsrate max. | 25 fps |
| IR-Sperrfilter | schaltbar |
| Lichtempfindlichkeit | 0,04 Lux, bei F1,2 |
| Low Speed Shutter | ja |
| Wide Dynamic Range (WDR) | WDR Dynamic Contrast |
| Objektiv Typ | Varifokal |
| Digital Zoom | ja |
| Beleuchtung | nein |
| Gehäuse | Innen |
| Farbe (Gehäuse) | schwarz |
| Gehäusematerial | Aluminium |
| Scheibenheizung | nein |
| Videoausgänge | nein |
| Alarmeingänge | 2 |
| Audiounterstützung | ja |
| Interner Speicher | microSD-Karte, microSDHC-Karte, microSDXC-Karte |
| Stromversorgung | 8-28VDC, PoE |
| Power over Ethernet | IEEE 802.3at |
| Vandalismusgeschützt | nein |
| Temperaturbereich (Betrieb) | 0°C ~ +45°C |
| Schutzart | keine Angabe |
| ONVIF | ja |
| Hersteller-Nr. | 01568-031 |

Zubehör

| AXIS T8007 PS24 | Netzteil, innen, 230VAC, 24VDC, 1,5A |
| --- | --- |
| AXIS T8640 POE+ OVER COAX KIT | Medienkonverter, RJ45, BNC, Ethernet über Koax, PoE+, Base-/Device Set (2 Stück) |
| AXIS T8129 POE EXTENDER | PoE Extender, PoE, PoE+ kompatibel, RJ45, 100m Reichweite |
| NETWORK CABLE COUPLER IP66 | RJ45 Koppler, Buchse-Buchse, für Außen, IP66 |
| AXIS T8604 MEDIA CONVERTER SWI | Ethernet Medienkonverter, 2x 10/100Mbps RJ45, 2x 100/1000Mbps SFP |
| AXIS T8123-E OUTDOOR MIDSPAN 3 | PoE Midspan, 1 Port, IEEE802.3at, 30W, IP66, -40°C - +55°C |
| NETWORK CABLE COUPLER INDOOR | RJ45 Koppler, Buchse-Buchse, nur für Innenraum |
| NETWORK CABLE COUPLER INDOOR S | RJ45 Koppler, Buchse-Buchse, nur für Innenraum, kompakte Ausführung |
| AXIS T8353A MICROPHONE 3.5MM | Mikrofon, omnidirektional, 3,5mm Klinkenstecker, diskrete Ausführung |
| AXIS T8351 MICROPHONE 3.5MM | Mikrofon, omnidirektional, 3,5mm Klinkenstecker, diskrete Ausführung |
| AXIS CONNECTOR A 2P3.81 STR 10 | Axis Anschlussblock, 2-polig, Stecker, Abstand: 3.81 mm, für Stromversorgung, 10 Stück |
| AXIS CONNECTOR A 4P2.5 STR 10P | Axis Anschlussblock, 4-polig, Stecker, Abstand: 2.50 mm, für I/O Ports, 10 Stück |
| AXIS T8133 30W MIDSPAN | PoE+ Midspan, IEEE802.3at, Type 2, Class 4, 1 Port |
| AXIS CONNECTOR A 2P2.5 STR 10P | Axis Anschlussblock, 10-polig, Stecker, Abstand: 2.50 mm, für I/O Ports, 10 Stück |
| AXIS T90B15 W-LED | LED Weißlicht Scheinwerfer, 5700K, 10-120°, austauschbare Linsen, 12/24V, 12W, IP66 |
| AXIS T90B20 IR-LED | LED Infrarot Scheinwerfer, 850nm, 10-120°, austauschbare Linsen, 12/24V, 24W, IP66 |
| AXIS T90B25 W-LED | LED Weißlicht Scheinwerfer, 5700K, 10-120°, austauschbare Linsen, 12/24V, 24W, IP66 |
| AXIS T90B30 IR-LED | LED Infrarot Scheinwerfer, 850nm, 10-120°, austauschbare Linsen, 12/24V, 48W, IP66 |
| AXIS T90B35 W-LED | LED Weißlicht Scheinwerfer, 5700K, 10-120°, austauschbare Linsen, 12/24V, 48W, IP66 |
| AXIS T90B40 IR-LED | LED Infrarot Scheinwerfer, 850nm, 10-120°, austauschbare Linsen, 12/24V, 96W, IP66 |
| AXIS T8134 60W MIDSPAN | High PoE Midspan, 1 Port, 60W, Gigabit, -10 - +45°C, 100-240V IEEE802.3at, IEEE802.3af |
| AXIS T8415 INSTALLATION TOOL | Installations Tool, zur Axis Kamera Einrichtung, WLAN, Akku, USB, PoE+, ONVIF |
| AXIS T8331 PIR MOTION DETECTOR | Infrarot Bewegungsmelder, passiv, Fläche, 12x12m, 85°, Innen, weiß, 12VDC |
| AXIS T8331-E PIR MOTION DETECT | Infrarot Bewegungsmelder, passiv, Fläche, 12x15m, 120°, außen, IP54, weiß, 12VDC |
| ACS CORE DEVICE E-LICENSE | Axis Camera Station Software, Version 5.x Core Device, E-Lizenz, 1 Kanal |
| ACS UNIVERSAL DEVICE E-LICENSE | Axis Camera Station Software, Version 5.x Universal Device, E-Lizenz, 1 Kanal |
| ACS 4 TO UNIVERSAL UPG E-LIC | Axis Camera Station, Upgrade Version 4.x nach 5.x Universal Device, E-Lizenz, 1 Kanal |
| ACS CORE TO UNIVERSAL UPG ELIC | Axis Camera Station, Upgrade Version 5.x Core to Universal Device, E-Lizenz, 1 Kanal |
| ACS 1 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 1 Kanal |
| ACS 4 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 4 Kanal |
| ACS 16 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 16 Kanal |
| ACS 32 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 32 Kanal |
| ACS 1 UNIVERSAL DEVICE LICENSE | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 1 Kanal |
| ACS 4 UNIVERSAL DEVICE LICENSE | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 4 Kanal |
| ACS 10 UNIVERSAL DEVICE LIC | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 10 Kanal |
| ACS 20 UNIVERSAL DEVICE LIC | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 20 Kanal |
| ACS 4 TO UNIVERSAL 1 UPG.LIC | Axis Camera Station, Upgrade Version 4.x to 5.x Universal Device, Lizenzcode, 1 Kanal |
| ACS 4 TO UNIVERSAL 5 UPG.LIC | Axis Camera Station, Upgrade Version 4.x to 5.x Universal Device, Lizenzcode, 5 Kanal |
| ACS 4 TO UNIVERSAL 10 UPG.LIC | Axis Camera Station, Upgrade Version 4.x to 5.x Universal Device, Lizenzcode, 10 Kanal |
| ACS 4 TO UNIVERSAL 20 UPG.LIC | Axis Camera Station, Upgrade Version 4.x to 5.x Universal Device, Lizenzcode, 20 Kanal |
| ACS CORE TO UNIVERSAL 1 UPGLIC | Axis Camera Station, Upgrade Version 5.x Core to Universal Device, Lizenzcode, 1 Kanal |
| ACS CORE TO UNIVERSAL 5 UPGLIC | Axis Camera Station, Upgrade Version 5.x Core to Universal Device, Lizenzcode, 5 Kanal |
| ACS CORE TO UNIVERSAL 10 UPGLI | Axis Camera Station, Upgrade Version 5.x Core to Universal Device, Lizenzcode, 10 Kanal |
| ACS CORE TO UNIVERSAL 20 UPGLI | Axis Camera Station, Upgrade Version 5.x Core to Universal Device, Lizenzcode, 20 Kanal |
| AXIS T8061 ETHERNET SURGE PROT | Überspannungsschutz, bis 10kV, für Netzwerkkomponenten, GBit und PoE Support, IP66 |
| AXIS SURVEILLANCE CARD 64 GB | Speicherkarte, microSDXC, 64GB, Class 10, 20 MB/s, inkl. SD-Adapter, Axis zertifiziert |
| AXIS T8516 POE+ NETWORK SWITCH | Gigabit Switch, managed, 16 PoE+ Ports, 2x SFP/RJ45 Uplinks, 240W PoE, 19", 1HE |
| AXIS T8611 SFP MODULE LC.LX | SFP Modul, Gigabit, 1310nm, Single mode, 10km, LC Anschluss |
| AXIS T8612 SFP MODULE LC.SX | SFP Modul, Gigabit, 850nm, Multi mode, 550m, LC Anschluss |
| AXIS T8613 SFP MODULE 1000BASE | SFP Modul, Gigabit, 1000BASE-T, RJ45 |
| AXIS SURVEILLANCE CARD 128G | Speicherkarte, microSDXC, 128GB, Class 10, 50 -100 MB/s, SD-Adapter, Axis zertifiziert |
| AXIS 4IN1 SECURITY SCREWDRIVER | Schraubendreher Set, 4-in-1, Biteinsätze pasend für Axis Produkte, inkl. Tasche |
| AXIS T8606 MEDIA CONV SWITCH 2 | Ethernet Medienkonverter, 2x 10/100Mbps RJ45, 2x 100/1000Mbps SFP, 24VDC |
| AXIS T93C10 OUTDOOR HOUSING | Wetterschutzgehäuse, für Axis Q16 und P13 Kameras, Aktive Kühlung, Heizung, IK10, IP66 |
| POWER SUPPLY PS24 240 W | Versorgungsnetzteil, 24VDC, 10A, 240W, 100-240 VAC, IP67, -40° - +70°C |
| AXIS T8144 60W INDUSTRIAL MIDS | High PoE Midspan, 1 Port, 60W, Gigabit, -40 - +75°C, 20-60VDC DIN Montage |
| AXIS T90D20 IR-LED | LED Infrarot Scheinwerfer, 850nm, 10-120°, austauschbare Linsen, 12-24V, 18W, IP66, IK9 |
| AXIS T90D20 POE IR-LED | LED Infrarot Scheinwerfer, 850nm, 10-120°, austauschbare Linsen, PoE, 20W, IP66, IK09 |
| AXIS T90D25 W-LED | LED Weißlicht Scheinwerfer, 6000K, 10-120°, austauschbare Linsen, 12-24V, 24W, IP66, IK9 |
| AXIS T90D25 POE W-LED | LED Weißlicht Scheinwerfer, 6000K, 10-120°, austauschbare Linsen, PoE, 25W, IP66, IK09 |
| AXIS T90D30 IR-LED | LED Infrarot Scheinwerfer, 850nm, 10-120°, austauschbare Linsen, 12-24V, 46W, IP66, IK9 |
| AXIS T90D30 POE IR-LED | LED Infrarot Scheinwerfer, 850nm, 10-120°, austauschbare Linsen, PoE, 49W, IP66, IK09 |
| AXIS T90D35 W-LED | LED Weißlicht Scheinwerfer, 6000K, 10-120°, austauschbare Linsen, 12-24V, 42W, IP66, IK9 |
| AXIS T90D35 POE W-LED | LED Weißlicht Scheinwerfer, 6000K, 10-120°, austauschbare Linsen, PoE, 47W, IP66, IK09 |
| AXIS T90D40 IR-LED | LED Infrarot Scheinwerfer, 850nm, 10-120°, austauschbare Linsen, 24V, 100W, IP66, IK09 |
| AXIS SURVEILLANCE CARD 128 GB | Speicherkarte, microSDXC, 128GB, Class 10, 50-80 MB/s, SD-Adapter, Axis zertifiziert |
| AXIS T8645 POE+ COAX COMPACT K | PoE+ über Coax Set, 1x AXIS T8641 Base Einheit, 1x AXIS T8643 Device Einheit |
| AXIS SURV CARD 128 GB 10PCS | Speicherkarte, microSDXC, 128GB, Class 10, 50-80 MB/s, Axis zertifiziert, 10 Stück |